- On a Windows based PC, download Update.zip and instructions.txt.

- Copy both the Update.zip and instructions.txt to an empty microSD card.  Do not unzip the Update.zip file.

- Power off your A100 tablet.

- Insert the microSD card into the A100 tablet.

- Press and hold the “Volume Down” key then press and hold the “Power” key.

- Once the “Power” key white LED turns on, release “Power” key but still hold “Volume Down” key.

- The Acer screen will appear and the tablet will vibrate.  Do not release “Volume Down” key until an "Erasing cache before SD update..." message appears in the upper left corner of the screen.

- The OS firmware is updated.  This process will take a few minutes.

- The A100 will automatically reboot when it is complete.

- The above steps reload the OS but do not erase customer data.  If you also wish to erase customer data, perform a “Factory data reset” (Apps > Settings > Privacy > Factory data reset > Reset Tablet).